## Slide 1: Chapter 2 The System Unit, Processing, and Memory

## Slide 2: Learning Objectives (1)
Understand how data and programs are represented to a computer and be able to identify a few of the coding systems used to accomplish this.
Explain the functions of the hardware components commonly found inside the system unit, such as the CPU, GPU, memory, buses, and expansion cards.
Describe how peripheral devices or other hardware can be added to a computer.
Understand how a computer’s CPU and memory components process program instructions and data.
2

## Slide 3: Learning Objectives (2)
Name and evaluate several strategies that can be used today for speeding up the operations of a computer.
List some processing technologies that may be used in future computers.

## Slide 4: Overview
This chapter covers:
  How computers represent data and program instructions
  How the central processing unit (CPU) and memory are arranged with other components inside the system unit
  How a CPU performs processing tasks
  Several strategies are used today to create faster and better computers today and in the future
4

## Slide 5: Data and Program Representation
    Digital data representation is the process of representing data in digital form so it can be understood by a computer
  Coding systems are used to represent data and programs in a manner understood by the computer
  Digital computers can only understand two states, off and on (0 and 1)

## Slide 6: Digital Data Representation
A bit is the smallest unit of data that a binary computer can recognize (a single 1 or 0)
A byte is equivalent to 8 bits
  Byte terminology used to express the size of documents and other files, programs, etc.
Prefixes are often used to express larger quantities of bytes: kilobyte (KB), megabyte (MB), gigabyte (GB), terabyte (TB), petabyte (PB), exabyte (EB), zettabyte (ZB ), yottabyte (YB)

## Slide 7: Representing Numerical Data: The Binary Numbering System
    The binary numbering system uses only two symbols (1 and 0) to represent all possible numbers
      The numbering system computers use
The decimal numbering system uses 10 symbols (0-9)
      The numbering system people use
In both systems, the position of the digits determines the power to which the base number (such as 10 or 2) is raised

## Slide 8: Example of the Decimal and Binary Numbering Systems

## Slide 9: Coding Systems for Text-Based Data: ASCII and EBCDIC
ASCII (American Standard Code for Information Interchange) is the coding system traditionally used with personal computers
  Most commonly uses 8 bits
EBCDIC (Extended Binary-Coded Decimal Interchange Code)
  Developed by IBM, primarily for mainframes

## Slide 10: Coding Systems for Text-Based Data: Unicode
Unicode
  Newer code consisting of 8 to 32 bits per character
  Universal coding standard designed to represent text-based data written in any ancient or modern language, as well as thousands of other symbols and signs
  Replacing ASCII as the primary text-coding system

## Slide 11: Coding Systems for Other Types of Data: Graphics Data
Graphics data (still images such as photos or drawings) consist of bitmapped images made up of a grid of small dots called pixels
  Monochrome graphic can only be one of two colors
    Requires just one bit for color storage
  Images with more than two colors
    Can use 4, 8, or 24 bits to store the color data for each pixel
  The number of bits per pixel depends on the type of image
    JPEG images taken by most digital cameras today use 24-bit true color images; large images can typically be compressed
    Common image formats include TIF, BMP, GIF, and PNG

## Slide 12: Representing Graphics Data

## Slide 13: Coding Systems for Other Types of Data: Audio and Video Data
Audio data must be in digital form in order to be stored on or processed by a computer
  Often compressed when sent over the Internet
    MP3 files are 10 times smaller than their uncompressed digital versions
    Compressed files download more quickly and take up less storage space
Video data is displayed using a collection of frames, each frame contains a still image
  Amount of data can be substantial, but can be compressed

## Slide 14: Representing Software Programs: Machine Language
Machine language is a binary-based language for representing computer programs the computer can execute directly
  Early programs were written in machine language
  Today’s computers allow programs to be written in a programming language, which is then translated by the computer into machine language in order to be understood by the computer

## Slide 15: Quick Quiz (1)
1. Another way to say “one trillion bytes” is _____.
  a. one gigabyte
  one terabyte
  one megabyte
2. True or False: MP3 files are stored using 0s and 1s.
3. The _____________ numbering system is used by computers to perform mathematical computations.

## Slide 16: Quick Quiz (1)
Answers:
b
True
binary

## Slide 17: Inside the System Unit
The system unit is the main case of a computer or mobile device
  Houses the processing hardware for a computer
  Also contains other components, such as storage devices, the power supply, cooling hardware, one or more processors, several types of memory, and interfaces to peripheral devices
  Interconnected through sets of wires called buses on the motherboard

## Slide 18: Inside a Desktop System Unit

## Slide 19: Inside a Tablet System Unit

## Slide 20: The Motherboard
The motherboard is a circuit board consisting of computer chips, also called integrated circuits (ICs)
  ICs contain interconnected components (such as transistors) to perform particular functions
  All devices connect via a wired or wireless connection to the motherboard
  External devices connect by plugging into a port
    The port is either built directly into the motherboard or created via an expansion card
  Wireless external devices use either a transceiver or wireless networking technology

## Slide 21: The Power Supply and Drive Bays
The power supply connects to the motherboard to deliver electricity
Portable computers use a rechargeable battery pack
    Built-in batteries more difficult and expensive to replace, resulting in electronic waste (e-waste)
Drive bays are rectangular metal racks inside the system unit that house storage devices
    Hard drive, CD/DVD drive, flash memory card reader
    Storage devices also connect to the motherboard

## Slide 22: Processors and the CPU
    A processor consists of circuitry and components packaged together and connected directly to the motherboard
The CPU (central processing unit) does the vast majority of processing for a computer
  Called a microprocessor when talking about personal computers
  Typically designed for a specific type of computer
    Desktops, servers, and some notebook PCs use Intel or Advanced Micro Devices (AMD) processors
    Portable computers and mobile devices often use Intel or AMD mobile processors or an ARM processor instead

## Slide 23: CPU Cores
Multi-core CPUs contain the processing components (cores) of multiple independent processors in a single CPU
Dual-core CPUs contain two cores
Quad-core CPUs contains four cores
Multi-core processors allow computers to work on more than one task at a time
  They also typically use slower cores than single-core CPUS so have fewer heat problems

## Slide 24: Examples of CPUs

## Slide 25: The GPU
The GPU (graphics processing unit) takes care of the processing needed to display images (including still images, animations) on the screen
  Can be located on the motherboard, on a video graphics board, or in the CPU package
  Mobile processors often integrate other capabilities into the processor package (system-on-a-chip (SoC))

## Slide 26: Technology and You
Modular Phones
Currently in development
Individuals create custom phones
Start with basic modules
Give the user flexibility to add, upgrade, or replace modules whenever
Google’s Project Ara
Google’s modular smartphone prototype.

## Slide 27: Processing Speed
Processing speed can be measured by the CPU’s clock speed
  Rated in megahertz (MHz) or gigahertz (GHz)
  Higher CPU clock speed = more instructions processed per second
  Alternate measure of processing speed is the number of instructions a CPU can process per second
    Megaflops (millions), gigaflops (billions), teraflops (trillions)
  Benchmark tests can be used to evaluate overall processing speed

## Slide 28: Word Size and Cache Memory
A computer word is the amount of data that a CPU can manipulate at one time
  In the past, CPUs used 32-bit words (referred to as 32-bit processors); today, most CPUs are 64-bit processors
Cache memory is a special group of very fast circuitry usually built into the CPU (internal cache memory)
  More cache memory typically means faster processing
  Cache memory level numbers indicate the order in which the various levels of cache are accessed by the CPU
    Level 1 is fastest, then Level 2, then Level 3

## Slide 29: Bus Width, Bus Speed, and Bandwidth
A bus is an electronic path over which data can travel
  Found inside the CPU and on the motherboard
  Bus width is the number of wires in the bus over which data can travel
    A wider bus allows more data to be transferred at one time
Bus width and bus speed together determine the bus’s bandwidth (the amount of data that can be transferred via the bus in a given time period)
The amount of data actual transferred under real-life conditions is called throughput

## Slide 30: Example of Bus Width

## Slide 31: Memory
Memory refers to chip-based storage, or locations that a computer uses to store data on a temporary basis
  Volatile memory (content is erased when the device is shut off)
  Non-volatile memory (content is retained when the device is shut off)
Random access memory (RAM) is the computer’s main memory or system memory
  Stores essential parts of operating system, programs, and data the computer is currently using
  Consists of electronic circuits etched onto chips
    Mobile devices typically use embedded memory chips
    Servers and personal computers use circuit boards called memory modules plugged into the motherboard

## Slide 32: Inserting RAM Memory Modules

## Slide 33: Characteristics of RAM
Volatile
Measured in bytes (amount dependent on CPU and operating system)
Most personal computers use SDRAM
Double-Data Rate (DDR) RAM sends data twice as often as ordinary SDRAM or prior versions of RAM
  DDR2, DDR3, DDR4
Dual-channel memory architecture has two paths that go to and from memory; tri-channel (three paths) and quad-channel (four paths) memory architecture used for higher performance

## Slide 34: Memory Addressing
Each location in memory has an address
  Usually stored in one or more consecutive addresses, depending on its size
Computer system sets up and maintains directory tables to facilitate retrieval of the data

## Slide 35: Registers and ROM
Registers are high-speed memory locations built into the CPU
  Used to store data and intermediary results during processing
  Fastest type of memory
ROM (read-only memory) consists of non-volatile chips located on the motherboard into which data or programs have been permanently stored
  Retrieved by the computer when needed
  Being replaced with flash memory

## Slide 36: Flash Memory
Flash memory consists of nonvolatile memory chips that can be used for storage
  Have begun to replace ROM for storing system information (BIOS)
  Stores firmware for personal computers and other devices
  Built into many types of devices (tablets, smartphones, and digital cameras) for user storage
  Built into some storage devices (solid-state hard drives, USB flash drives, etc.)

## Slide 37: Fans, Heat Sinks, and Other Cooling Components
Fans are used on most personal computers to help cool the CPU and system unit
  Heat is an ongoing problem for CPU and computer manufacturers
    Can damage components
    Cooler chips run faster
Heat sinks are small components typically made out of aluminum with fins that help to dissipate heat
Some portable computers and virtually all mobile devices don’t include a fan; instead thermal transfer materials are used to spread out the heat generated

## Slide 38: Other Types of Cooling Systems
Liquid cooling systems
  Cool the computer with liquid-filled tubes
Immersion cooling
  Hardware is actually submerged into units filled with a liquid cooling solution
Notebook cooling stand
  Cools the underside of a notebook computer
Other cooling methods, such as ion pump cooling systems, are under development

## Slide 39: Examples of Computer Cooling Methods

## Slide 40: Expansion Slots and Expansion Cards
An expansion slot is a location on the motherboard into which expansion cards are inserted
An expansion card is a circuit board inserted into an expansion slot
  Used to add additional functionality or to attach a peripheral device
Smaller devices may integrate capabilities directly into the device
USB adapters can be used with portable computers and some mobile devices

## Slide 41: Examples of Expansion Cards and Adapters

## Slide 42: Buses
A bus is an electronic path within a computer over which data travels
  Located within the CPU and etched onto the motherboard
An expansion bus connects the CPU to peripheral (typically input and output) devices
The memory bus connects the CPU directly to RAM
The frontside bus (FSB) connects the CPU to the chipset that connects the CPU to the rest of the bus architecture

## Slide 43: Examples of Buses and Expansion Slots

## Slide 44: PCI, PCIe, and USB
The PCI bus used to be the most common type of expansion bus
Today, PCI Express (PCIe) buses are more common
  PCIe x16 is a 16-bit bus and is used to connect monitors to a computer
  PCIe x1 is a 1-bit bus and is used to connect other peripherals
  PCIe buses are extremely fast
A universal serial bus (USB) connects USB devices to a computer
  127 different devices can connect via a single USB port
  Extremely versatile

## Slide 45: Ports and Connectors
A port is a connector on the exterior of a computer’s system unit to which a device may be attached
  Typical desktop computer ports HDMI to connect a monitor (VGA and Digital Video Interface (DVI) are older standards)
  Network ports connect a device to a wired network
  USB ports connect USB devices; can be USB-C
  Others include IrDA and Bluetooth ports, flash memory card slots, audio ports, eSATA ports, and Thunderbolt ports (Apple)
  Most computers support the Plug and Play standard
  USB and Thunderbolt devices are hot-swappable

## Slide 46: Examples of Typical Ports and Connectors

## Slide 47: USB Hubs
USB hubs connect multiple devices to a single USB port

## Slide 48: How It Works
USB-C
Both ends of a USB-C cable are the same
  Traditional USB cables have two different connectors:
    USB-A and USB-B
Very fast
Can charge and power portable computers
Many types of adapters and multiport adapter cables available
USB-C ports are oval shaped; cables are reversible and interchangeable.

## Slide 49: Ports and Connectors: Tablets and Smartphones
Tablets have ports similar to desktop computers, but often not as many
  Connecting a tablet to a tablet dock can provide additional connectivity options
Smartphones have more limited expansion capabilities
  Usually have a USB port
  Some have a flash memory card slot
  Some have a Subscriber Identify Module (SIM) slot to hold a SIM card

## Slide 50: Examples of Typical Ports for Tablets and Tablet Docks

## Slide 51: Quick Quiz (2)
1. Which type of memory is erased when the power goes out?
  a. ROM
  b. RAM
  c. flash memory
2. True or False: The CPU can also be called the motherboard.
3. An electronic path within a computer over which data travels is called a(n) _____________.

## Slide 52: Quick Quiz (2)
Answers:
B
False
bus

## Slide 53: How the CPU Works
The CPU (central processing unit) consists of a variety of circuitry and components packaged together
  The transistor is the key element of the microprocessor
    Made of semi-conductor material that controls the flow of electrons inside a chip
    Today’s CPUs contain hundreds of millions of transistors; the number doubles about every 18 months (Moore’s Law)
  Electronic impulses move from one part of the CPU to another to process data
  The architecture and components included in a CPU (referred to as microarchitecture) vary from processor to processor

## Slide 54: Inside the Industry
Moore’s Law
In 1965, Gordon Moore predicted that the number of transistors per square inch on chips had doubled every two years and that trend would continue
Moore’s Law is still relevant today for processors as well as other computer components
George Moore (1970)

## Slide 55: CPU Core Components
The arithmetic/logic unit (ALU) performs arithmetic involving integers and logical operations
The floating point unit (FPU) performs decimal arithmetic
The control unit coordinates and controls activities within a CPU core
The prefetch unit attempts to retrieve data and instructions before they are needed for processing in order to avoid delays

## Slide 56: CPU Core Components (cont’d)
The decode unit translates instructions from the prefetch unit so that they are understood by the control unit, ALU, and FPU
The registers and internal cache memory store data and instructions needed by the CPU
The bus interface unit allows the core to communicate with other CPU components

## Slide 57: Inside a CPU Core

## Slide 58: The System Clock
  The system clock is a timing mechanism within the computer system that synchronizes the computer’s operations
  Located on the motherboard
  Sends out a signal on a regular basis to all computer components
  Each signal is a cycle
  Number of cycles per second is measured in hertz (Hz)
  One megahertz = one million ticks of the system clock

## Slide 59: Clock Speed
Computers can run at a multiple or fraction of the system clock speed
  Many PC system clocks run at 200 MHz; all devices run at a fraction or multiplier of the clock speed
  A CPU clock speed of 2 GHz means the CPU clock “ticks” 10 times during each system clock tick
  During each CPU clock tick, one or more pieces of microcode are processed
  A CPU with a higher clock speed processes more instructions per second than the same CPU with a lower CPU clock speed

## Slide 60: The Machine Cycle
A machine cycle occurs whenever the CPU processes a single piece of microcode
  It consists of four operations:
    Fetch
    Decode
    Execute
    Store

## Slide 61: Making Computers Faster and Better Now and in the Future
Improving the Performance of Your System Today
  Add more memory
  Perform system maintenance
    Uninstall programs properly
    Remove unnecessary programs from the Startup list
    Place unneeded large files on external storage
    Delete temporary files
    Error-check your hard drive
    Scan for viruses and spyware
    Clean out the dust

## Slide 62: Making Computers Faster and Better Now and in the Future (cont’d)
  Buy a larger or second hard drive
    Can be internal or external
    Move files from your primary drive to make it faster
  Upgrade your Internet connection
    Various types of connections and speeds are available
  Upgrade your video graphics card
    PCs with integrated graphics can typically have a graphics card added
    Graphics cards can be upgraded if needed
    Some notebooks switch to integrated graphics when using battery power to extend battery life

## Slide 63: Strategies for Making Faster and Better Computers: Pipelining
Pipelining allows multiple instructions to be processed at one time
  A new instruction begins as soon as the previous instruction completes a stage of the machine cycle

## Slide 64: Multiprocessing and Parallel Processing
Using more than one processor or processor core is common today
  Multiprocessing: Each processor or core typically works on a different job to process these jobs faster than with a single processor
  Parallel processing: Multiple processors or cores work together to process a single job as fast as possible
  Multithreading: the ability of a CPU (or software) to execute multiple streams of instructions (called threads) within a single program at the same time

## Slide 65: Improved Architecture and Materials
Improved architecture
  Smaller components, faster memory, faster bus speeds, increasing number of CPU cores, integrated GPUs, support for virtualization, and increased 3D graphics processing
Improved materials
  Traditionally, CPUs used aluminum circuitry on silicon chips
  Alternate materials include copper chips, and high-k, germanium and other III-V materials
  Graphene consists of flat sheets are carbon one atom tall
    Lightest and strongest known material
    Graphene chips are faster than silicon chips and require less power

## Slide 66: Improved Architecture and Materials (cont’d)
Improved materials (cont’d)
  Flexible electronic components
    Can be bent without damaging circuitry
    Thinner, lighter, generate less heat, and consume less power than conventional processors
    Needed for flexible devices, wearable clothing, etc.

## Slide 67: Trend
Smart Clothing
Is the next trend in wearable technology
Contains flexible circuitry and sensors, wireless connectivity, and a battery
Can monitor your physical activity
  Transmits 3D information about your activities
  Syncs data to your smartphone
Smart fabric is under development
Smart fabric.

## Slide 68: 3D Chips
3D chips pack a number of components layered onto small chips
  Cuts down on the surface area required
  Especially important with notebook computers and mobile devices
  Memory cells are stacked on top of one another in layers
  For CPUs, the transistors are layered

## Slide 69: Nanotechnology
Nanotechnology is the science of creating tiny computers and components less than 100 nanometers in size
  Carbon nanotubes (CNTs) are tiny, hollow tubes of graphene
  Great potential for many applications
    Used in TVs, solar cells, light bulbs, consumer products like surfboards, and computing products like memory
    Carbon nanotube fibers conduct heat and electricity like a metal wire
    Nanofilters that can remove contaminants from water sources
    Nanosensors that can detect cancer-causing toxins or cancer drugs inside single living cells

## Slide 70: Examples of Nanotechnology

## Slide 71: Terascale/Exascale Computing
High-performance computing (HPC)
  Terascale computing is the ability of a computer to process one trillion floating point operations per second (teraflops)
    Research is focusing on creating multi-core processors with tens to hundreds of cores used in conjunction with multithreaded hardware and software to achieve teraflop performance
  The next development is expected to be exascale computing that can process data at exaflop (1,000 petaflops) speeds

## Slide 72: Quantum Computing
Quantum computing applies the principles of quantum physics and quantum mechanics to computers
  Utilizes atoms or nuclei working together as quantum bits (qubits)
  Qubits function simultaneously as the computer’s processor and memory and can represent more than two states
  Used for specialized applications, such as encryption and code breaking

## Slide 73: Optical Computing and Silicon Photonics
Optical computers use light to perform digital computations
  Can be smaller and faster than electronic computers
  Opto-electronic computers use both optical and electronic components
Silicon photonics uses light for data transfers within and among silicon chips
  Expected to be used to transfer very large quantities of data at very high speeds between chips in servers, mainframes, and supercomputers

## Slide 74: In-Class Discussion
Define ROM (read-only memory). What is one important difference between ROM and RAM (random access memory)?
What are the general operations of a machine cycle?
Discuss the design a hypothetical computer of tomorrow, the equivalent of a desktop or notebook PC today. How big would the computer be? Would it be portable or built into furniture or some other object? Should it be wearable or embedded in a person’s body? What is the ideal computer of the future?
Discuss products that use computer chips and microprocessors today. What functions the chips provide to their stated products? Discuss other products that would benefit from the inclusion of a processor in the future? What about products that would be improved if they included built-in computer processing abilities?